DYNAMIC ROUTING
Access list
access-list 20 deny 192.168.2.3
access-list permit any
int fa 0/0
ip access-group 20 in
conft
router rip
version 2
network [netwrok id]
network 192.168.2.0 255.255.255.0
network 10.0.0.0 255.0.0.0

VLAN
Creating vlan (Each switch)
conft
vlan 10
name student
vlan 20
name admin
Assigning vlan to each port
int fa0/0
switchport mode access
switchport access vlan 10
Assigning trunk line for communication
int fa 0/4
switchport mode trunk
switchport trunk access vlan 1-99
DHCP
ip dhcp pool network1[or name]
network 192.168.10.0 255.255.255.0
server system
service configuration

OSPF (DYNAMIC ROUTING)
1st router
router ospf 1
network [nid] [subnet mask complement] area0
network [nid] [subnet mask complement] area0
network [nid] [subnet mask complement] area0

2nd router
router ospf 2
network [nid] [subnet mask complement] area0
network [nid] [subnet mask complement] area0
network [nid] [subnet mask complement] area0

3rd router
router ospf 2
network [nid] [subnet mask complement] area0
network [nid] [subnet mask complement] area0

Static Routing
Each Router
ip route [network id] [subnet] [router port ip through which information need to pass]
ip route [network id] [subnet] [router port ip through which information need to pass]